2.2.7 	Axiom Glass Channel

- Product/Manufacturer:  Axiom – Glass Channel; Armstrong World Industries, Inc.

- Component:  Extruded aluminum alloy 6063. The component is extruded in a channel form to provide a glazing channel designed as a transition between a glazed partition and the acoustical ceiling systems.  Factory applied baked polyester paint. Custom RAL powder coated finish to match.

  - Acceptable product: Armstrong Axiom Glazing Channel for Partitions item (AXGC) (AXGCV) (AXGCS) (AXGCD), 2” inch high interior glass partition channel

    - Acceptable Suspension systems:

      - Armstrong World Industries: Prelude, Prelude Plus, Suprafine, Interlude, Silhouette, Sonata, Clean Room, Drywall Furring System and suspension system members.

    - Acceptable Acoustical Ceiling Panels:

      - Armstrong World Industries Ceiling Panels designed with Tegular Edges

      - Armstrong World Industries Ceiling Panels designed with Vector Edges

- Accessories:

  - Axiom Splice Plate (AX4SPLICE):  Galvanized steel finish; formed to fit into special bosses and locked in place with 4 factory-installed screws.

  - Axiom Cross Tee Clip (AXCCLT): to join suspension system components to the Axiom – Glass Channel.